## Slide 2: ALTO New Transport using HTTP/2 draft-schott-alto-new-transport-01
Roland Schott
Y. Richard Yang
Kai Gao
Jensen Zhang
March 23, 2022
IETF 113

## Slide 3: Outline
Motivation and requirements
ALTO/H2 design
Discussions and open issues

## Slide 4: Motivation
ALTO base protocol [RFC7285] is an HTTP/1.x client-pull protocol
ALTO/SSE [RFC8895] adds incremental server push using Server-Sent-Event, but is based on HTTP/1.x
  Need additional control connection
  Updates must be serialized
RFC8895 IESG review
  Consider HTTP/2
------------------------------------------------------------------
| |
| +-------+ +-------+ 1. init request +------+ |
| | | | | <------------- | | |
| | | | | -------------> | | |
| 3.add/ | | | | 1'. control uri | | |
| remove | | | | | | |
| resource |Stream | |Update | | | |
-------->|Control| private |Stream | 2a. data update |Client| --
|Server |<------->|Server | messages | |
-------- | | | | --------------> | | <-
| response | | | | --------------> | | |
| | | | | 2b.control update| | |
| +-------+ +-------+ messages +------+ |
| |
------------------------------------------------------------------

## Slide 5: ALTO/H2 Design Requirements
From ALTO base protocol [RFC 7285]
  R0: Client can request any ALTO resource using the connection, just as using ALTO base protocol using HTTP/1.x
From ALTO SSE [RFC 8895]
  R1: Client can request the addition (start) of incremental updates to a resource
  R2: Client can request the deletion (stop) of incremental updates to a resource
  R3: Server can signal to the client the start or stop of incremental updates to a resource
  R4: Server can choose the type of each incremental update encoding, as long as the type is indicated to be acceptable by the client
From ALTO base framework [RFC 7285]
  R5: Design follows basic HTTP Representational State Transfer architecture if possible
    Can use only a limited number of verbs (GET, POST, PUT, DELETE, HEAD)
  R6: Design takes advantage of HTTP/2 design features such as parallel transfer and respects HTTP/2 semantics [PUSH_PROMISE]
Allow flexible deployment
  R7: Capability negotiation

## Slide 6: Outline
Motivation and requirements
ALTO/H2 design
  Overview

## Slide 7: ALTO/H2 Transport Information Structure
ALTO Server
Information resource
Transport queue
Incremental updates queue
Receiver set
New
Existing
C1
C2
C3
Clients
Static resource such as CostMap
Filterable resource such as FilteredCostMap
tq1
tq1/uq
tq2
tq3
ir1
tq1/rs
A single HTTP/2 connection between each client and the server
INT/
HTTP/2
HTTP/2
C3
tq4
IPv4 headers

## Slide 8: Futuristic SIGCOMM Challenge: Channel Spec
Multiple cases
  L3/4: Information bits that already exist in the datapath, indicate the information
    IPv4 header fields, DSCP, IPv4/6 options, tunneling protocol headers
  Cross: Information bits that can be defined in a programmable network
    P4 INT bits
  L1/2: In particular in wireless, which Freq, Time Multiplexing, sends the network information
A way to define a universal (cross-layer) schema to specify the network information channel (https://; …)
Hierarchy, dependency
Security properties
  Dummy design
Datapath packets:
  can be lost (dummy: add redundancy); packet pattern may not be regular (dummy: send dummy packets)
  Intermediates: HTTP based streaming server -> client => HTTP based streaming server -> revers proxy nginx -> client

## Slide 9: A Framework to Transport Network Info to App

## Slide 10: Main Todo
Specify the mapping of incr to physical bits (streams, e.g., HTTP/2, HTTP/3, IPv4/6 bits, …)
Need to do in a separate document
Write a SIGCOMM’22 NAI
Call for adoption of HTTP/2
Forward to request art review [http/2 feedback, but also http/3 feedback]

## Slide 11: ALTO/H2 Transport Information Structure
Client opens a connection to the server
Client opens/identifies a transport queue tq
  Client requests transport queue status
  Client requests an element in the message queue
  Client becomes a receiver
  Client receives push updates
Client closes the transport queue
Client closes connection

## Slide 12: Outline
Motivation and requirements
ALTO/H2 design
  Overview
  Transport queue

## Slide 13: Transport Queue
Basic operations (CRUD): create, read (get status), delete
Client creates transport queue
  POST to transport queues path
    Request reuses ALTO/SSE input
      HTTP :method=post with AddUpdateReq [RFC8895]
    Response
      <transport-queue> // add error codes, …, txt add error handling spec; give a pointer that stream management will be given in later section
Client reads transport queue: GET <transport-queue>
Client closes transport queue:
  Explicit: DELETE <transport-queue>
    Delete from local view (server may still maintain the transport queue for other client connections)
  Implicit: Transport queue for a client is ephemeral: close of connection or stream deletes the transport queue from the client’s view --- when the client reconnects, the client MUST NOT assume that the queue is still valid
Notes: The HTTP stream that created a transport queue is kept open until the stream is deleted or a non-recoverable error associated with the transport queue happens
  The stream should be closed

## Slide 14: Transport Queue Example (Create)
Client -> Server request
Server -> Client response

## Slide 16: Slightly Extreme Design
First use flow service to specify a flow
  Endpoint flow cost service [L3, L4, 5Gtunnel]
    Identifier: [srcIP, dstIP, sPort, dPort, protocol] => ECN
    srcIP, dstIP => IPoption
    Cost metric: ECN
Create a transport queue
  Map incr update queue to the data path spec
    incremental update queue (virtual queue embedded into the IPv4 stream)
      IPv4/6:ECN bits, TCP transport options
  Receiver set

## Slide 17
SEND header transport-mapping-directive
SEND header-fields !end-stream
Specify mapping to HTTP/2

## Slide 18: Transport Queue Example (Read)
Client -> Server request
Server -> Client response

## Slide 19: Outline
Motivation and requirements
ALTO/H2 design
  Overview
  Transport queue
  Incremental updates queue

## Slide 20: Incremental Updates Queue
Incremental updates queue basic operations (CRUD): read (get status)
  Client cannot create, update, or delete incremental updates queue directly---it is read only, and associated with transport queue automatically
  Read:
    Input: <tq>/uq
    Response: updates queue state // TODO: error
      Add schema; responses have tags;
      What if the seq number runs out
      Seq# is integer,
    Note
      Server determines the state (window of history and type of each update) in the update queue [R4]
      Read of updates queue status allows client to know
        backlog status
        workload to catch up (HEAD)
        potential direct link
Request
Response data

## Slide 21: Outline
Motivation and requirements
ALTO/H2 design
  Overview
  Transport queue
  Incremental updates queue
  Individual updates

## Slide 22: Individual Incremental Updates
Individual incremental updates operations (CRUD): pull read or push read
  Client pull
    GET <update-uri>
  Server push
    Initialization:
      the first update pushed from the server to the client MUST be the later of the following two
        the last independent update in the incremental updates queue
        the following entry of the entry that matches the tag when the client creates the transport queue
      The client MUST set SETTINGS_ENABLE_PUSH to be consistent
    State: the server maintains the last entry pushed to the client and schedules next update push
      Per client, connection state
    Client MUST NOT cancel (RST_STREAM) a PUSH_PROMISE
      To avoid complex server state management

## Slide 23: Client Pull Example

## Slide 24: Server Push Initialization Example
First push, if client has no matching tag
First push, if client has tag matching previous entry

## Slide 25: Server Push Transport Example
Each pushed update is indicated first in a PUSH_PROMISE

## Slide 26
src
Network controller
ALTO client (app controller)
ALTO server (app controller)
Cong bit client -> server
dst

## Slide 27
client
server
Network controller
ALTO client (app controller)
ALTO server (app controller)
Cong bit client -> server; cschannel = HTTP/2

## Slide 28
sender
receiver
ALTO client
ALTO server
Cong bit client -> server; cschannel = IPV4:ecn

## Slide 29
client
server
ALTO client (app controller)
ALTO server (app controller)
Cong bit client -> server; cschannel = IPV4:ecn
Info CP
Info DP
Instantiation
IPv4/v6
5G tunnel
P4
Socket API
..
Compression
Authentication
Raw info
sketch

## Slide 30: Key Design Points – Dummy Design
Network node
  FlowSpec Which packets (e.g., L3: IPv4, IPv6; L4: TCP flow, QUIC)
    Dummy one is OpenFlow to specify flow match condition, or some IETF spec
  LHS = RHS (e.g., x = a * 5; x = x + 5) { flow.<var> = <expr> //}
  InfoSpec What info is put into (e.g., queue length) Yang model
    RHS A set of attributes which is well specified, e.g., queue length, ECN, … (IANA numbers)
    Instruction set: read, write, add, incr, count, sketch, … (very small crud)
  FormatSpec In what format (existing or new)
    LHS (address of the packet header space) IPv4 ECN bit, IPv4 optional header, IPv6 header (wireshark packet field spec)
  WhenSpec When (e.g., every packet, sampling function, …)
    When vocabulary: every packet|sample function (1/n, random…, )

## Slide 31: Unified, App-Driven Network Monitoring [ALTO]
<match> <lhs> := <rhs>
  Simple mapping to ipv4/ipv6
  Compile to p4 headers
    { p4 header spec; p4 language } INT
  Apps
    ecn
    HPCC (style; Alibaba/Harvard)
    Demonstrate the benefit of joint coding between off-path and on-path
      Off-path sends the long term info, and on-path sends the updates

## Slide 32: Application-Driven Data-Intensive Data Sciences [Position]
Introduction
Architecture
Modeling
  Jacob: make a model on the transport prediction [formulation]
Control
  Scheduling system
    QoE aware scheduling (bi-level) [Alex, Jensen]
Initial performance eval – mininet based eval
Replication (Rucio)
Access Layer
Science Workflows (Panda, HTCondor)
App Transport System (FTS): scheduling
xrootd, gridftp: basic 3rd transport
TCP/network transport

## Slide 33
Spec to use datapath for network info exposure consists of the following:
  FlowSpec InfoSpec FormatSpec WhenSpec
  Datapath-control: { flowspec:
  infospec:
  formatspec:
  whenspec: }

## Slide 34
<send-condition> <flow-selector> <LHS-pkt> := <RHS>
<update-local-state-cond> <flow-selector> <LHS-state> := <RHS>
Update condi
Update the local state
pkt
send

## Slide 35
Match | Action
FlowSpec | Mark the info to be sent to the app Already typed system, e.g., IPv4 header format-><var> = <value> <- info Generic container // C struct, ie.., union data type <var>.attr = value

## Slide 36: TODOs
Benefit analysis (settings)
  Gap analysis (appendix to specify)
Challenges
  Leverage existing packet formats

## Slide 37
Fast information (mostly INT)

## Slide 38: Outline
Motivation and requirements
ALTO/H2 design
  Overview
  Transport queue
  Incremental updates queue
  Individual updates
  Receiver set

## Slide 39: Receiver Set
Receiver set operations (CRUD): read (get status), delete (self only)
By default a client can see only itself in the receiver set
  Appearance of self in the receiver set (read does not return not exists) is an indication that push starts
A client can delete itself (stops receiving push):
  Explicit: DELETE <transport-queue>/rs/self
  Implicit: Transport queue is connection ephemeral: close of connection or stream for the transport queue deletes the transport queue (from the view) for the client

## Slide 40: Outline
Motivation and requirements
ALTO/H2 design
  Overview
  Transport queue
  Incremental updates queue
  Individual updates
  Receiver set
  Stream management

## Slide 41: ALTO/2 Stream Management: Objectives
Objectives
  Allow stream concurrency to reduce latency
  Minimize the number of streams created
  Enforce dependency among streams (so that if A depends on B, then A should be sent before B)
    Encode dependency to enforce semantics (correctness)
TODO/Appendix: how to handle/map to HTTP/3 QUIC

## Slide 42: ALTO/H2 Stream Management: Specification
Client -> Server [Create transport queue]
  Each request to create a transport queue (POST) MUST choose a new client selected stream ID (SID_tq)
    Stream Identifier of the frame is a new client-selected stream ID; Stream Dependency in HEADERS is 0 (connection) for an independent resource, the other transport queue if the dependency is known
    Invariant: Stream keeps open until close or error

## Slide 43: ALTO/H2 Stream Management: Specification
Client -> Server [Close transport queue]
  DELETE to close a transport queue (SID_tq) MUST be sent in SID_tq
    Stream Identifier of the frame is SID_tq; Stream Dependency in HEADER is 0 (connection)
      So that a client cannot close a different stream
      HEADERS indicates END_STREAM; server response also close stream

## Slide 44: ALTO/H2 Stream Management: Specification
Client -> Server [Request on data of a transport queue SID_tq, e.g., read message]
  Stream Identifier of the frame is a new client-selected stream ID, Stream Dependency in HEADERs MUST be SID_tq
    So that a client cannot issue request on a closed transport queue
    Request indicates END_STREAM; response also indicates end of stream

## Slide 45: ALTO/H2 Stream Management: Specification
Server -> Client PUSH_PROMISE for transport queue SID_tq
  PUSH_PROMISE sent in stream SID_tq to serialize to allow the client to know the push order
  Each PUSH_PROMISE chooses a new server-selected stream ID
    Stream is closed after push

## Slide 46: Concurrent Streams Management
Controlled by SETTINGS_MAX_CONCURRENT_STREAMS
Client -> Server
  There is one stream for each open transport queue
    A client can always close a transport queue (it uses the open stream) and hence can open -> can close, without issue of deadlock
Server -> Client push
  Each push needs to open a new stream

## Slide 47: Outline
Motivation and requirements
ALTO/H2 design
  Overview
  Transport queue
  Incremental updates queue
  Individual updates
  Receiver set
  Stream management
Discussions and open issues

## Slide 48: Transport and Pub/sub
What is missing
  The design does not allow creation of generic message queues
  Only the server can be the publisher
    Clients publish info to be shared with other client
  The design does not have the capability of Exchange (message router)
Way forward: Keep simple
  Broker for further discussion
https://www.rabbitmq.com/resources/specs/amqp0-9-1.pdf

## Slide 49: Additional Information about Transport Queue
Calendar semantics
  Tell the client ALTO information (e.g., cost) for a future time point
  Tell the client when the next information will be released, it is the time that the info is released is distributed, not the value [support]

## Slide 50: Open Issues
Make a two-layered design [Need update]
  Base layer
  Instantiation into HTTP/2 and HTTP/3 separately
Base Design (tq, uq, rs, …)
HTTP/2
HTTP/3

## Slide 51: Decision
Separate base layer
First get a complete first version for HTTP/2
Next or earlier look into HTTP/3
  Two sides of issues
    Neg: HTTP/3 flexibility may cause issues for our design
    Pos: HTTP/3 allows more flexibility which we can benefit from
Current design
  PUSH_PROMISE are sent in the open stream and they all follow the same order
  HTTP/3 allows all to be concurrent

## Slide 52: HTTP2 -> HTTP/3 Issues
HTTP/2 frames are serialized into a single FIFO, reliable TCP connection
  http2-send(stream-id, msg1) followed by http2-send(stream-id, msg2);
    We know that msg1 will arrive before msg2
HTTP/3 frames use independent UDP data connections

## Slide 53: Negotiation
Task: to fully specify the complete set of negotiation parameters
  Use HTTP/2 (default), HTTP/3
  Incremental updates queue encoding
    Chosen by server, but must be specified as HTTP Accept header of client
      Initial connection setup: client sends list of incr update mime types, and server returns the subset which it can use (Vary header in response)
  Concurrency level (e.g., Rucio controller need to monitor info for a large number of clients) stream control

## Slide 54: Backup Slides

## Slide 55
Service | Type (Out if not labeled) | Core Information Structures | Main Size Var | Stability Expectation | Incremental Changes
Information Resource Directory [RFC7285] | application/alto-directory+json | Key-value store; Delegation | #resources | Stable | Add/delete resources
Network Map [RFC7285] | application/alto-networkmap+json | Key-value store: pid -> addrType -> array | #CIDRs | Stable | Add/delete CIDR from pid
Cost Map [RFC7285] | application/alto-costmap+json | Key-value store: srcPID -> dstPID -> value Depend on network map | #SRCPID * #DSTPID | More dynamic than network map | Update cost map entries
Filtered Map Services [RFC7285] | In: application/alto-networkmapfilter+json Out: application/alto-costmapfilter+json | In: selected srcPID, dstPID Key-value store: srcPID -> dstPID -> value Depend on network map | Filtered #SRCPID * #DSTPID | More dynamic than network map | Update cost map entries
Endpoint Property Service [RFC7285] | In: application/alto-endpointpropparams+json Out: application/alto-endpointprop+json | In: addr + prop Key-value store: addr -> prop -> value | #addr * #prop | Depend on property, can be dynamic or stable | Update property value
Endpoint Cost Service [RFC7285] | In: application/alto-endpointcostparams+json Out: application/alto-endpointcost+json | In: srcAddr x dstAddr Key-value store: srcAddr -> dstAddr -> value | #src * #dst | Can be more dynamic than cost map | Update cost value
Cost Calendar [RFC8896] | Extension to CostType | Calendar array | Previous * #num_intervals | Can be dynamic | Calendar window moves
Unified Property | In: application/alto-propmapparams+json; Out: application/alto-propmap+json | In: addr, prop Key-value store: addr -> prop -> value | #addr * #prop | Depend on property, can be dynamic or stable | Update property value
Path Vector | In: see costmap; Out: multipart/related;type=application/alto-costmap+json, | Cost map + unified property map | #src * #dst * #vec size | Depend on metric, can be dynamic or stable | Update path vector
CDNi Cap & Footprint | application/alto-cdni+json | Array; {capability-type: capability-value} | #footprint * #capability | Can be dynamic, bursty | Update capabilities

## Slide 56: Performance and Effectiveness of Current Transport
Infrastructures | Basic Workload (ALTO SPEC) | Transport | Collecting metrics
Benocs is fully open to use its infrastructure as an evaluation environment Greater Bay Network is also fully open to use its infrastructure as an evaluation environment | (Filtered) Cost map: distribute inter-site performance metrics and calendar; routing changes + link dynamics => updated metrics Endpoint/unified property service: endpoint access status query/updates/bwe CDN node footprint & capability Flow direction (pointing to CDN nodes) using ECS Path vector providing available reservable bandwidth | HTTP/1.x per request full retrieval keep alive pipelining HTTP/2, HTTP/3 per request, full retrieval ALTO/SSE RFC8895 (on HTTP/1.x) | ALTO Server processing load ALTO client processing load Transport load (bytes) Transport latency Throughput Scalability

## Slide 57: General Space of Network->App Information Transport
Protocol/Base Reference | What information | How transported | Frequency
ALTO/RFC7285, RFC8895 | Network map, cost map, unified property, … | HTTP/1.x client/server | Request/response; ALTO/SSE incremental push
ECN/RFC3168 | Congestion notification | 2 bits in IP Traffic Class header; ECN-Echo/CWR flags in TCP header | Per packet marking
NEF, SCEF<->AS/3GPP, … | Network capabilities/events -> AF | HTTP | Request/response
… |  |  | 

## Slide 58: Working Items
JSON-LINK as data model [TBD]
Benchmarking deployment and initial reports [Richard, Danny]
  openalto.org
  Open platforms, all are welcome to join
Initial draft surveying of Net->App information and transport in major SDOs [Roland, Chunshan, Richard]

## Slide 59
The value 0x0 is reserved for frames that are associated with the connection as a whole as opposed to an individual stream.

## Slide 60: Outline
High-level goal: openalto development, deep involvement of CERN team
Tool: NAI submission(s)

## Slide 61: Direction 1: Systematic Optimization
BW Allocation Formulation
Bi-Level Opt: Lower level is the real network BW alloc
BW Allocation Formulation
DNN Modeling (GNN Model)
+ Adjust if the model is not accurate, introduce DNN to adjust
BW Allocation Formulation
DNN Modeling
+ Adjust if the model is not accurate, introduce DNN to adjust
z,ztz = 1
Blackbox Closed-Loop Control
O(1/k) -> O(d/k)

## Slide 62
What’s new, what is substantial (hard)? What is the benefit?
Automatic workflow 3.3 use case (opt, QoE function, minimize the control overhead/leverage underlying fairness as much as possible)
Intro
Problem definition (flows are fixed and long term)
Overview and framework
Eval
Conclusion and future

## Slide 63: Direction 2
Focus on batch setting first
Formulation
  A set of rules {Ri}
    Ri: a set of current sources Si, a super set of candidates Ci, and need to pick Di \subset Ci s.t. |Di| = ni
      E.g., 2 nodes (Si) have data item i already, Ci nodes (4 nodes) can potentially host the data, and the target is have to 4 copies
        Pick 2 from Ci
        Note: it can be more complex, for example, pick one copy from EU, one from NA, …
    Each Rule Ri has a rule completion time RCTi
    Compute the optimal selection and scheduling of transfer rates
      F{RCTi} // assume a simple min_SelxSch {max RCTi} // average might be in that it can extended to incremental case // later consider download; goal is robustness; later add download
    Technical content
      NP hard (proof is a nugget; bin packing)
      How to come up w/ a reasonable algorithm

## Slide 64: Complexity
Selection problem Select Di out of Ci
  Millions of rules, Ci can be on the order of tens of nodes, Di might be only 2 or 3
Bandwidth estimation problem
  BW allocation (cubic, max-min) //
Future
  Rules can be dynamic (users add new data and their rules)

## Slide 65: TODO: Lower Bound
Dummy lower bound: the finishing time [bear 1]
  Assume each node is rate limited only at the edge; no bottleneck in the internal network
  Total supply of upload bw of all sources
    Mi is the file size for data item I
      Sum_i(Mi * ni) / Sum(BWUij) // this bound can be loose

## Slide 66: TODO: Initial Alg (Strawman I)
Step 1: assume the Di’s are chosen // main criticism: per rule auto
  Scheduling problem: each dst in Di will maintain a connection with each src and other members of Di
  Chop the file into fixed chunks (64M, 16M)
  Assume the list at download j is Lj (potential sourcers), each member in Lj has a state rj (moving average of downloading rate)
    Each interval T (10 sec)
      Swarm will exchange bit map about chunk availability
      Each will request from those chunks that it needs
      Each will unchoke the top 4 sourcers
      If (it is the 3rd interval) one of the 4 is a random to be unchoked

## Slide 67: TODO: Initial Alg (Strawman IIa)
Step 1: assume the Di’s are chosen and routes are given
Millions of rules, but only 10s or at around lower 100 nodes
Formulation
  Virtual nodes to link each rule Ri’s sources
  Add a destination for each rule and dst
System state at any instance
    Set of flows are VS_i -> VS_ij … -> Tdik if Tdik has not finished downloading
    When a dst finishes downloading, the flows for the dst are deleted
TDij
VS_i

## Slide 68: TODO: Initial Alg (Strawman IIb)
Step 1: assume the Di’s are chosen and routes are given
Millions of rules, but only 10s or at around lower 100 nodes
Formulation
  Virtual nodes to link each rule Ri’s sources
  Add a destination for each rule and dst
System state at any instance [finished dst can become a src]
    Set of flows are VS_i -> {VS_ij} … -> Tdik if Tdik has not finished downloading
    When a dst finishes downloading, the flows for the dst are deleted
TDij
VS_i
Notes: 10^6 rules, 2 srcs each rule and 3 dst each rule: 10^6 * 2 * 2 flows in a graph of 10s-100s of nodes;

## Slide 69: Aggregation and Compact
Virtual-node flows a few millions
Representation:
  (src_phy, dst_phy, #n)

## Slide 70: Technical Content
Assumption
  Case 1: Can rate limit each flow as needed [upper bound of potential]
    Assignment 1: come up the best alg you can
  Case 2: running a congestion control protocol + tc for a small number K of flows [real deployment]
    Assignment 2: give an initial alg for this setting
      BitTorrent alg [BEAT this; swarming, 70%]
  Case 2: max min fairness [conceptual]
Content:
  Design a control plane for the scheduling framework (replicated, consistency, multi-domain, fault tolerance)
  Simple greedy alg:
    Kai’s greedy alg which picks the maximum flow
  Eval: the performance of the alg compared to simple alg

## Slide 71: Basic Formulation
di in Di, pick the lowest cost si in Si using ALTO cost map

## Slide 72: Design 1
Order: 10s-100s of sites; can be millions of rules i
Fixed set Di from Ci is already given; sij -> dik (sizes) is given
Step 1: Compute the bw allocation to each flow using max-min fairness (the state will change as a flow finishes)
  Aggregation // as quickly as possible
    Initial solution:
      Aggregate the flows according to src-dst RSE pairs (100x100 10K)
        Input becomes <src-dst-rse-pair, #flows>
          For each link, compute the fair share (L_C / sum(#flows, src-dst-rse-pair uses link L)
          …

## Slide 73: Naïve Design 1
Naïve data structure
  Each flow is identified by an flow id
  Each flow’s route is stored in an array indexed by flow id, route[1][0], … index links
  Each flow’s size is stored in an array indexed by flow id size[flow_id]
Water-filling using naïve data structure will be very bad
  Loop // Major places for improvements: (1) incremental max-min, lower the #flows
    compute_fair_share of each
    compute the finishing_time of each flow // compute w/ the min (size_f / r_f)
    remove the flow from the flow list
  Compute share
    Foreach link l // total #link times #links * (2 #flows + # links)
      Scan the route array
        flow_counts[L] ++ if route[i][j] == L // compute the
      Compute fair share
        Lset = argmin(L: C[L]/flow_counts[L] ) // more like heap priority queue // optimization
      Scan the route array
        route[i][k] == DELETED if route[i][j] == L

## Slide 74: Naïve Design 2-3
Based on 1
  Aggregate the flows by src-dst-rse-pairs // Q: how to store the sizes
  // likely depends on the special structure of max-min fairness
  Incremental bottleneck structures
  Even “parallel-structure” of computation

## Slide 75: Design 4
Compute the rate when it is not max-min fair share
  NUM design // go back to optimization, but we want to explore the algorithmic side first
  TCP Cubic/Reno
    Assign each link a loss rate p_l
    Each flow’s rate: alpha MSS / RTT / \sqrt(q_i)
      q_f ~ sum p_l
    If the bottlenecks are at the edges, then it may not be too bad

## Slide 77: Alg.
Initialization
  Each link has a loss of fully utilize total capacity for shortest RTT

## Slide 78: Remaining Issues to be Done
Selection of Ci
…

## Slide 79: Stability Condition
Finite system: S1, … SN, and the system must drain all flows by T
  Stability condition for any j: \sum Si_{i=j, N} <= C (T – Tj)
Sj
Sj+1
Sj+2
SN
Define backlog upon flow I arrival
  Service curve definition
    A(t) – S(t) will not go to infinity

## Slide 80
Arrival curve